## Slide 1
ESCS'26 / CSCE'26
Real-Time PCB Defect Detection for Embedded Visual Inspection
A same-split comparison of YOLO11s and RT-DETR-L
Aditya Varun Dhayapulay and Paul Salvador Inventado California State University, Fullerton
1

## Slide 2
MOTIVATION
Why PCB Inspection Is Hard
ESCS'26 | 2
Small visual defects must become actionable locations
INSPECTION RISK
small defects
missing holes, shorts, spurs
OUTPUT NEEDED
boxes + classes
not image-level labels
Defects can become more expensive after assembly.
Localization supports review, repair, and process analytics.
A useful detector must balance recall, box quality, and latency.

## Slide 3
GOAL
Research Question
ESCS'26 | 3
Under one controlled PCB defect split, how do YOLO11s and RT-DETR-L compare for real-time visual inspection?
INPUT
PCB image
MODELS
YOLO11s vs RT-DETR-L
OUTPUTS
boxes, classes, metrics
Deployment-oriented: accuracy, localization, latency, and failure behavior.
Contribution is a reproducible benchmark, not a new detector architecture.

## Slide 4
CONTRIBUTIONS
What the Camera-Ready Version Adds
ESCS'26 | 4
01
Preserves practical comparison
YOLO11s-1280 vs RT-DETR-L-640
02
Adds matched resolution
YOLO11s-640 vs RT-DETR-L-640
03
Tests high-res RT-DETR-L
1280 px, batch size 1
04
Fixes per-class semantics
canonical class-ID mapping
05
Adds deployment artifact
Hugging Face Space demo
Practical result + controlled evidence + honest deployment scope.

## Slide 5
DATASET
Dataset and Defect Taxonomy
ESCS'26 | 5
Missing hole
Mouse bite
Open circuit
Short
Spur
Spurious copper
TRAIN IMAGES
5,551
deterministic split
VALIDATION
1,016
2,106 instances
TEST
1,016
2,179 instances
BALANCING
800
copy-paste train images
All reported configurations use the same validation and test image assignments.

## Slide 6
PROTOCOL
Reproducible Evaluation Protocol
ESCS'26 | 6
1
Hardware
Tesla V100-SXM2-32GB
2
Software
Ultralytics 8.4.51 / PyTorch 2.5.1
3
Evaluation
batch 1, workers 0, no TTA
4
Metrics
P, R, F1, mAP50, mAP50-95, latency
Baseline gate: archived checkpoint metrics must reproduce within 0.001 before new experiments are trusted.
Observed differences were approximately 10⁻⁸, confirming exact split/evaluator reproduction.

## Slide 7
PROTOCOL
Models and Training Settings
ESCS'26 | 7
Configuration | Image size | Epochs | Batch | Purpose
YOLO11s original | 1280 | 50 | 12 | accepted practical
RT-DETR-L original | 640 | 10 | 4 | accepted practical
YOLO11s controlled | 640 | 50 | 12 | matched resolution
RT-DETR-L controlled | 640 | 10 | 4 | matched resolution
RT-DETR-L high-res | 1280 | 10 | 1 | high-res analysis
The 1280-pixel RT-DETR-L run completed; the planned 960-pixel fallback was not needed.

## Slide 8
REVIEWER RESPONSE
The Key Fairness Issue: Resolution
ESCS'26 | 8
Accepted practical setup
YOLO11S
1280 px
more spatial detail
RT-DETR-L
640 px
lower input resolution
Useful as a deployment comparison, but not an architecture-only ablation.
Camera-ready fix
MATCHED
640 vs 640
same split and evaluator
HIGH-RES RT
1280 px
separate analysis
Separates practical configurations from resolution-controlled evidence.

## Slide 9
RESULTS
Accepted Practical Comparison
ESCS'26 | 9
Model | P | R | F1 | mAP50 | mAP50-95 | Total ms
YOLO11s 1280 | 0.880 | 0.866 | 0.873 | 0.902 | 0.502 | 15.2
RT-DETR-L 640 | 0.886 | 0.839 | 0.862 | 0.887 | 0.470 | 49.8
Recall
YOLO11s
0.866
RT-DETR-L
0.839
higher is better
mAP50-95
YOLO11s
0.502
RT-DETR-L
0.470
stricter localization
Total latency
YOLO11s
15.2
RT-DETR-L
49.8
milliseconds; lower is better
Interpretation: practical deployment choice among completed configurations.

## Slide 10
RESULTS
Matched-Resolution Results
ESCS'26 | 10
Model | P | R | F1 | mAP50 | mAP50-95 | Total ms
YOLO11s 640 | 0.870 | 0.852 | 0.861 | 0.892 | 0.482 | 13.2
RT-DETR-L 640 | 0.867 | 0.839 | 0.853 | 0.881 | 0.462 | 49.0
Recall
YOLO11s
0.852
RT-DETR-L
0.839
same 640 px resolution
mAP50-95
YOLO11s
0.482
RT-DETR-L
0.462
same evaluator
YOLO11s remains slightly stronger on recall and strict mAP while remaining much faster in this measured setup.

## Slide 11
RESULTS
High-Resolution RT-DETR-L Finding
ESCS'26 | 11
Model | P | R | mAP50 | mAP50-95 | Total ms
RT-DETR-L 640 | 0.867 | 0.839 | 0.881 | 0.462 | 49.0
RT-DETR-L 1280 | 0.766 | 0.534 | 0.604 | 0.295 | 74.4
MAP50-95 CHANGED
0.462 -> 0.295
did not improve
TOTAL LATENCY
49.0 -> 74.4 ms
higher cost
INTERPRETATION
separate row
not the matched comparison
More pixels alone did not compensate for the fixed high-resolution training setup and computational cost.

## Slide 12
RESULTS
Per-Class Behavior at 640 px
ESCS'26 | 12
Class | YOLO R | RT R | YOLO mAP50-95 | RT mAP50-95
Missing hole | 0.986 | 1.000 | 0.569 | 0.567
Mouse bite | 0.763 | 0.765 | 0.403 | 0.403
Open circuit | 0.850 | 0.880 | 0.525 | 0.513
Short | 0.892 | 0.865 | 0.551 | 0.505
Spur | 0.767 | 0.729 | 0.381 | 0.342
Spurious copper | 0.853 | 0.795 | 0.462 | 0.443
Strong classes
Missing hole, Open circuit, Short
Harder classes
Mouse bite and Spur remain subtle
Per-class analysis matters because aggregate mAP can hide inspection risk.

## Slide 13
QUALITATIVE AUDIT
Representative Successes
ESCS'26 | 13
SELECTION
class-balanced
matched YOLO11s-640
Shows localization across the six-class taxonomy.
Bounding boxes support review and repair workflows.
Visual audit complements aggregate metrics.

## Slide 14
QUALITATIVE AUDIT
Representative Failure Cases
ESCS'26 | 14
SELECTION SCORE
5FN + FP
miss-weighted audit
False negatives are prioritized because missed defects are costly.
Small/subtle classes motivate high-resolution reinspection.
mAP50-95 exposes loose localization that mAP50 may hide.

## Slide 15
DEPLOYMENT
Online Deployment Artifact
ESCS'26 | 15
Hugging Face Space
adiivd-pcb-defect-detection.hf.space
Browser workflow: upload PCB image, run detector, inspect annotations, download results.
Demonstrates packaging and usability.
Reports class counts, confidence values, and annotated detections.
Not an embedded-device benchmark.
No Jetson/TensorRT latency claims.

## Slide 16
SCOPE
Limitations and Future Work
ESCS'26 | 16
Current scope
V100 latency, not edge latency.
Same split, but not fully resource-normalized.
In-distribution data, not factory-domain validation.
Next steps
Real factory captures and lighting variation.
Resource-normalized training and latency budgets.
High-resolution crop reinspection.
Jetson/TensorRT benchmarking when hardware is available.

## Slide 17
CLOSE
Takeaways
ESCS'26 | 17
PRACTICAL RESULT
YOLO11s-1280
higher recall, mAP50-95, lower latency
CONTROLLED RESULT
YOLO11s-640
competitive at matched resolution
DEPLOYMENT LESSON
compare carefully
resolution and latency both matter
A deployment-oriented benchmark should separate completed configurations from controlled ablations.
Thank you. I welcome your questions.
Aditya Varun Dhayapulay | California State University, Fullerton